## Slide 1: Arsenic in the waters and sediments of the Humboldt River
Brittany Segill

## Slide 2: Where?
This study is taking place in Nevada, with particular interest in the Humboldt River and Humboldt River basin
This basin has various metallic and non-metallic economic deposits and is a leading producer of gold, silver, copper, mercury and tungsten in the US
The River and Basin also play a huge role in providing valuable sources of water for mining, construction, power plants, and municipal water supply

## Slide 3: Why?
Many previous studies have reported elevated concentrations of arsenic in multiple surrounding river waters of the Humboldt River Basin but not specifically the Humboldt River
  Carson River
  Walker River
  North Fork Humboldt River
This Arsenic has accounted for weathering of geologic material, hydrothermal sources and drainage through mined waste rocks
This study’s goal is to understand the processes controlling arsenic distribution between sediments and waters of the Humboldt River

## Slide 4: Sample sites
Many samples were taken nearby the intersection of highways and the river
Samples were taken during the dry season

## Slide 5: Background Geology of the area
The Upper Humboldt River has Miocene volcanic and sedimentary rocks with some pre-tertiary volcanic rocks
The Middle Humboldt River contains relatively widespread tertiary volcanic and cenozoic sedimentary rocks and widespread quaternary, alluvium, and lacustrine deposits
There are several geothermal hot springs in the Lower Humboldt River region
The Lower Humboldt River consists of quaternary alluvium and playa deposits, lake evaporites and lacustrine deposits
Notes: There are several geothermal hot springs in the Lower Humboldt River region
There are several geothermal hot springs in the Lower Humboldt River region
The Lower Humboldt River consists of quaternary alluvium and playa deposits, lake evaporites and lacustrine depositsThe wer Humboldt River consists of quaternary alluvium and playa deposits, lake evaporites and lacustrine deposit

## Slide 6: Testing Methods
Inductively Coupled Plasma-Mass Spectrometer (ICP-MS)
  Used to analyze major cations and trace elements
  For concentrations of total elements in sediment samples
Ion Chromatography
  To analyze major anions
Micromass Iso Prime stable isotope ratio mass spectrometer
  For stable isotope analysis for Deuterium and Oxygen-18

## Slide 7: Testing Methods continued
Eurovector elemental analyzer interfaced to a MIP stable isotope ratio mass spectrometer
  For sulfur-34 of dissolved sulfate analysis
X-ray powder diffractometry and Scanning Electron Microscopy
  Used to determine mineralogical associations in samples that contained high or low concentrations of arsenic
Web Based Hydrograph Analysis Tool
  Used to determine the fractions of direct runoff and groundwater inflows from the streamflow data

## Slide 8: Test results

## Slide 9: More in depth results
The river water is alkaline and oxic
pH of 8.64-9.13 (Basic)
Oxidation-reduction potential is 10-192.4 mV
Conductivity of 720-1280 μS/cm
Concentrations of Arsenic range from 0.012 to 0.066 mg/L with an average of 0.03 mg/L
Stable isotopes range from -7.5 to -15.7‰ for Oxygen-18 and -85 to -125‰ for deuterium

## Slide 10: In depth results continued
The most abundant minerals are quartz, orthoclase feldspar, calcite, biotite, and muscovite
Further testing showed some silicate and detrital aluminum silicate clay minerals
About 83% of total Arsenic is extracted from the residual fraction, which corresponds to silicate and clay minerals
The relative dominance of Al (64%), Ca (70%), and Fe (82%) in the residual fraction can be accounted for silicate and clay minerals

## Slide 11: Arsenic in Sediments
The occurrence of the arsenic is because of the As-bearing iron oxyhydroxides which naturally occur in many parts of the world
The occurrence of As in Fe-Mn oxides and hydroxides have been previously reported in other studies close to this area
However, As in silicate minerals in the river sediments, which is near-surface and oxidizing, has not been reported previously
The results found in this study suggest that silicate mineral phases predominantly control As distribution in the Humboldt River sediments

## Slide 12: Arsenic in Water
The As levels were compared to when it is low-flow season to high-flow season
The concentrations of As are not affected significantly so changes in As concentrations in different parts of the Humboldt River reflect different geochemical and physical processes without significant seasonal perturbations
Another study in the region suggested oxidation of mined waste rocks containing As-bearing sulfide minerals as the primary source for high dissolved As and SO4 in the waters

## Slide 13: Conclusions
The primary source for dissolved As in the upper Humboldt River is due to the oxidation of As-bearing sulfide minerals from metal-ore deposits
Dilution of As and SO4 in the middle Humboldt River is due to subsequent mixing of river water with discharging groundwater
Localized mixing of geothermal and As-rich groundwater increases dissolved As concentrations in the waters in the Lower Humboldt River

## Slide 14: Conclusions
Dissolved As occurs from evaporative enrichment of the lower river region because of the favorable arid and temperate climate
As distribution in the river sediments is controlled by partitioning onto silicate clay minerals
  This implies the risk for potential immobilization of As in groundwater with change in geochemical conditions to reduce conditions. This warrants future studies to investigate the region

## Slide 15: Any Questions?

## Slide 16: References
Mohammad, Shahnewaz, and Regina N. Tempel. “Arsenic in the Waters and Sediments of the Humboldt River, North-Central Nevada, USA: Hydrological and Mineralogical Investigation.” Environmental Earth Sciences, vol. 78, no. 17, 2019, doi:10.1007/s12665-019-8552-1.