| HW #11: Spectra, Lasers, Solid State Physics Assigned: 5/5/10 Due: 5/12/10 | Introductory Modern Physics (95.210) Spring 2010 Instructor: Prof. Wasserman Olney 126 daniel_wasserman@uml.edu (978) 934-4530 |
| --- | --- |

- A 3-level laser system is pumped from the ground state (0) to the upper laser state (2) by a HeNe laser (632nm), which excites 1018 electrons/cm3-s to state 2 (R02).   Assume the separation between the ground state and this excited state is the energy of the HeNe.  Electrons can then transition down to state 0 or state 1 (the lower laser state).  The nonradiative scattering time between 2-1 is 100ps (tnr21) and between 2-0 is 250ps (tnr21), and the spontaneous emission time between 2-1 is 1ns (t21).  State 1 is 120meV above state 0, with a scattering time of t10=1ps.  Assume there the vast majority of electrons are in state 0, and even with the pumping to higher state, the total population of state 0 doesn’t change.  There is a thermal excitation from state 0 to state 1, at a rate of 1016 electrons/cm3-s.

  - In the absence of an external field (you still have the HeNe, but no other light, for argument’s sake), determine the steady state densities of the three states.  Hint: the rate of change for the population of a given state i, for a given process n is Ni/tn.  In steady state, the total population change of a state should be 0.

  - Do you have population inversion?  What is the minimum R02 required to achieve population inversion?

  - Now determine the total number of photons/s emitted by the spontaneous emission from 2-1 at population inversion, and compare the spontaneously emitted power to the incident pump power.

  - Now assume you have a population inversion N2-N1=1018 cm3.  What is the pump rate required to achieve this population inversion, in the absence of an external field.

  - Now imagine you include the effects of the external field at the frequency corresponding to the 2-1 transition, what is the density of the external field which will reduce your population inversion to half of its original (N2-N1=5E17)?  Remember, the induced transition rate B12*u(f)=B12*u(f)=c3u(f)/(8πhf3tspont).

- Calculate the position and widths (in E) of the first 2 energy bands and band gaps in a 1D crystal modeled as 0.1nm quantum wells separated by 0.2nm barriers of potential height 1eV.

- T&L

10-6, 9, 11, 14, 18, 20, 27, 30, 33, 38, 40