## Slide 1: Heavy Metal Contamination History of Renuka Lake
Sarah Perkins

## Slide 2: About the Lake
Between the Lesser Himalaya sedimentary rocks
  Dolomitic limestone, slate, quartzite, calcareous, carbonate, shale, sericite, etc.
150-200 cm of rainfall annually
Main sources of water are from monsoon rain and underground seepage

## Slide 3: Introduction
Purpose- Determine the heavy metal contamination history of Renuka Lake from 1893-2003
Reason- Himalayan lakes are facing an acute problem of survival due to an increase in toxic elements in the water and sediments
Goal- To understand the heavy metal load and possible sources

## Slide 4: Materials and Methods
Sampling
ICP-MS analysis

## Slide 5: Dating
210Pb
  Half life of 22.26 years
  Supported 210Pb from surrounding rocks
  Unsupported 210Pb from atmosphere
137Cs
  Half life of 30 years
  Maximum fallout in 1963

## Slide 6: Statistical Analysis
Contamination factor
Degree of contamination

## Slide 7: Statistical Analysis
Geo-accumulation Index
Pollution load index

## Slide 8: Results
210Pb
  Top 0-19 cm  2011-1974
    Sedimentation rate= 0.51 cm/yr
  19-37 cm  1974-1950
    Sedimentation rate= 0.78 cm/yr
  Average sedimentation rate= 0.64 cm/yr
137Cs
  Highest concentration at 37.5 cm 1963
  Sedimentation rate= 0.79 cm/yr

## Slide 9: Results
Lead, chromium, cobalt, copper, zinc, and nickel all showed similar trends from 2003-1839 but with different amplitudes

## Slide 10: Results- Lead (Pb)
Natural sources
  Detrital quaternary sediments (K-feldspar, plagioclase, carbonates)
  Shale
  Lake based sulfide minerals
Anthropogenic sources
  Vehicle emissions
  Acid batteries
  Paints
  Sewage

## Slide 11: Results- Chromium (Cr)
Natural sources
  Quartzite
  Chlorite
Anthropogenic sources
  Stock farms
  Industries
  Agro-chemicals

## Slide 12: Results- Cobalt (Co)
Natural sources
  Olivine
  Pyroxine
  Mica
  Garnet
Anthropogenic sources

## Slide 13: Results- Copper (Cu)
Natural sources
  Silicates
  Carbonates
  Copper sulfides
  Other evaporate minerals
  Enriched in shale
Anthropogenic sources
  Coal burning
  Atmospheric deposition
  Vehicle emissions
  Gas, diesel, and lubricant combustion

## Slide 14: Results- Zinc (Zn)
Natural sources
Anthropogenic sources
  Metal plating and related works

## Slide 15: Results- Nickel (Ni)
Natural sources
  Mafic and ultra mafic rocks
Anthropogenic sources
  1975- metallic waste dumping

## Slide 16: Results- Manganese (Mn)
Natural sources
  Shale
  Dolomite
Anthropogenic sources
  Burning fossil fuels
  Sewage
  Mining

## Slide 17: Results- Contamination Factors

## Slide 18: Results- Positive Correlation
Strong
  Cr- Cu, Ni, Pb
  Cu- Zn, Ni, Pb
  Zn- Ni, Pb
  Ni- Pb
Moderate
  Cr- Zn
  Co- Cr, Cu, Ni, Pb

## Slide 19: Results- Comparison

## Slide 20: Conclusion