## Slide 1
Chapter 2 Basic Laws
A typical circuit in Chapters 2, 3:
We will be asked to find some of the variables: v1, v2, v3, v4, i1, i2, i3.
We need three basic Laws:
Ohm’s law
Kirchhoff’s current law (KCL)
Kirchhoff’s voltage law (KVL)
Chapter 2 will use these laws to solve simple circuits
Chapter 3, 4, develop systematic methods to solve complex circuits.
L3

## Slide 2
§ 2.2 Ohm’s Law – Property of a resistor
A resistor:
Circuit Symbol
Notation
R
Suppose voltage v and current i are assigned according to passive convention
Ohm’s Law: Voltage across a resistor is directly proportional to the current flowing through it: v  i,  v / i = constant.
Resistance: is defined as the ratio v/i, i.e.,
Measured in ohm () 1 = 1V/A
For a resistor
Sometime active sign convention cannot be avoided:
L3

## Slide 3
Material | ρ (Ω•m) at 20 °C
Silver | 1.59×10−8
Copper | 1.68×10−8
Gold | 2.44×10−8
Aluminium | 2.82×10−8
Calcium | 3.36×10−8
Zinc | 5.90×10−8
Nickel | 6.99×10−8
Lithium | 9.28×10−8
Iron | 1.0×10−7
Material | ρ (Ω•m) at 20 °C
Carbon | 4×10−5 to 8×10−4
Germanium | 4.6×10−1
Sea water | 2×10−1
Drinking water | 2×101 to 2×103
Silicon | 6.40×102
Material | ρ (Ω•m) at 20 °C
Glass | 10×1010 to 10×1014
Hard rubber | 1×1013
Sulfur | 1×1015
Air | 1.3×1016 to 3.3×1016
Teflon | 10×1022 to 10×1024
Resistance depends on the material and structure
For a material with cross-sectional area A and length ,
* is the resistivity, measured in
Resistivity for some conductors:
Semi-conductors:
Insulators:

## Slide 4
Two special resistors:
R= 0, v = Ri=0.
No matter how much current flows in it, no voltage drop  a short circuit.
A wire made of conductor can be considered as a short circuit.
R= ∞, i = v/R =0.
No current flows in it for any voltage.  an open circuit.
Usually two disconnected points, or two points separated by insulator.
Types of resistors:
  Fixed resistor,
  Variable resistor
  Linear resistor
  Nonlinear resistor
We only consider fixed linear resistors.
Conductance: The reciprocal of resistance
Measured in mho, or Siemens (S)
Conductance measures the ability to conduct electric current.
With the same voltage applied, larger conductance yields larger current.
Power consumed by a resistor:
L3
Always consumes power

## Slide 5
§ 2.3 Nodes, branches, loops
Branch: represents a single element, a source or a resistor.
For the above circuit, there are 5 branches.
Node: a point connecting two or more branches, or a group of points, a piece of wire, where there is no voltage drop.
The above circuit has only 3 nodes.
Node 1
Node 3
Node 2
L3

## Slide 6
An equivalent circuit can be drawn to clearly show the nodes
Node 1
Node 2
Node 3
A piece of wire can be replaced with a single point.
Node 1
Node 3
Node 2
Loop: any closed path.
It is hard to count all loops.
In chapter 3, we use mesh, a simple loop that does not contain any other loop in it.
L3
Node 3

## Slide 7
§ 2.4 Kirchhoff’s Laws
KCL: Kirchhoff’s current law
KVL: Kirchhoff’s voltage law.
Both established in 1847
KCL is based on the law of conservation of charge.
KCL Law:
the algebraic sum of currents entering a node (or a closed boundary ) is 0.
Sum of currents leaving = sum of currents entering
Closed boundary
L3
” for entering
for leaving

## Slide 8
Application: use KCL to combine currents.
i1
i3
i0
i0+ i1-i2+i3= 0,
 i0= i2-i1-i3
i2-i1-i3
i1
12 A
12 A
i2
i3
8 A
9 A
a
b
c
d
Example: Use KCL to find i1,i2,i3
KCL at node a:
8 - 12- i1= 0
 i1= -4A
At node c:
9-i2-8 = 0,
 i2=1A
At node d:
i3+12-9=0,
 i3= -3A
L3

## Slide 9
KVL is based on the law of conservation of energy.
KVL law:
The algebraic sum of all voltage drops around a loop, along
clockwise (or counter clockwise) direction, is zero.
+ v2 -
+
v3
-
+ v1 -
- v4 +
-
v5
+
Along clockwise direction:
From + to - : voltage drop
From – to + : voltage rise
All are voltage drop.
By KVL,
v1+v2+v3+v4+v5= 0
- v2 +
+ v1 -
+ v4 -
+
v5
-
+
v3
-
By KVL, v1-v2+v3-v4-v5= 0
L3
For voltage drop, use “+”
For voltage rise, use “-”
+ v2 -
- v4 +
Voltage drop: v1, v3
Voltage rise: v2,v4,v5
-
-v5
+

## Slide 10
Loop 1
Loop 2
Loop 3
Loop 4
KVL along loop 3
2+5-v4=0, v4=7V
Loop 4: v3+v4+4=0, v3=-11V
Loop 1:
v1-v3-3=0, v1=-8V Loop 2: -v2-2-v1=0, v2=6V.
Example:
L3

## Slide 11
Use KVL to add up voltages:
+
v1
-
-
v2
+
-
v3
+
a
b
+
vab
-
Make a loop to include the open circuit from b to a.
KVL along clockwise direction,
v1-v2-v3-vab= 0,
The voltage drop from a to b is the sum of voltage drops along a path from a to b.
vab= v1-v2-v3
Given what is
L3

## Slide 12
Practice problem 1: Find in the following circuits
5
3A
(a)
+
-
2
5V
(d)
+
-
3k
5V
(c)
+
-
4k
5V
(b)
Ohm’s Law:
R3

## Slide 13
+
-
10V
3
5
2A
Practice 2: Find

## Slide 14
Basic Laws
L4
Ohm’s Law:
KVL law: the algebraic sum of all
voltage drops around a loop, along
clockwise (or counter clockwise)
direction, is zero.
- v2 +
+ v1 -
+ v4 -
+
v5
-
+
v3
-
By KVL, v1-v2+v3-v4-v5= 0
For voltage drop, use “+”
For voltage rise, use “-”
KCL Law: the algebraic sum of currents
entering a node (or a closed boundary )
is 0.
” for entering
for leaving

## Slide 15
Use basic laws to solve simple circuit problems.
Example: Find current I and vab .
L4
Main idea:
Transform the circuit problem into a math problem: using all three basic laws to make an equation for current I.
We need to assign auxiliary variables to make each step clear.
We assign resistor voltages, v1, v2.
I
a
b
+ -

## Slide 16
Solution:
1) By KCL, same current flows through all elements in clockwise direction.
2) Voltage for each element is either given, or, can be expressed in terms of the current I, by Ohm’s law.
Use KVL to form an equation:
(E2)
Plug (E1) into (E2) to obtain equation for I
For vab, by KVL, .
Since , ,
we obtain

L4
How to find
Alternatively, work on left side loop
I
I
(E1)
I
a
b
+ -

## Slide 17
What if some resistor voltages are assigned the opposite way?
Let us reverse
Use KVL to form an equation:
Plug (E1) into (E2) to obtain equation for I
 18I=, I= 1.5A
L4
Same equation for :
I
a
b
+ -
I
I
(E1)
For , use KVL

## Slide 18
Key point: Find a key variable so that you can express other variables in terms of it. Then you can use KVL, or KCL and ohms Law, to make an equation for it. For the previous circuit, I is the key variable.
Example: Find vx and the power supplied by the 3A source.
4
3
4
2
0.5vx
3A
Main idea:
Express branch currents in terms of vx.
Then use KCL at node a to form an equation for vx.
L4
a

## Slide 19
3
I1
I2
I1
I2
I2
4
4
2
0.5vx
3A
a
Solution: Assign current I1 and I2.
To find power supplied by 3A,
assign v3A. By KVL,
v3A=v1+vx+v2 = 2I2+vx+3I2
=2+4+3=9V
Thus, p3A=-93=-27W.
Power supplied.
Question: Can you find from KVL along left side loop?
By KCL, same I1 flows through upper 4 and dependent current source.
How to express in terms of ?
I1=0.5vx (E1).
How to express in terms of ?
Also by KCL, same current I2 flows through the 3
resistors in the right loop.
Thus by Ohm’s law,
I2=vx/4 (E2)
Use KCL at node a, I1+I2=3.
Plug in (E1), (E2), to obtain
0.5vx+vx/4=3,  vx=4V
With vx=4V, have I2=vx/4=1A
Q: How many different currents?
L4
is a current. Huge mistake to put current in a KVL equation

## Slide 20
3
I1
I2
I1
I2
I2
4
4
2
0.5vx
3A
a
Main steps:
1) Assign currents I1 and I2.
a) By property of the dependent source
I1=0.5vx (E1).
b) By Ohm’s law,
I2=vx/4 (E2)
4) Plug (E1), (E2) in (*) to obtain
0.5vx+vx/4=3,  vx=4V
L4
2) Use KCL at node a,
I1+I2=3 (*)
3) Express in terms of
Main idea:
Express branch currents in terms of vx.
Then use KCL at node a to form an equation for vx.
Summary:
With computed, you can find
And all resistor voltages and source voltages ,
And the power by each element

## Slide 21
3
I1
I2
I1
I2
I2
4
4
2
0.5vx
3A
a
Another approach: use I2 as key variable
L4
KCL at a: (E1)
Another way to express in terms of ?
(E2)
Plug (E2) into (E1)

## Slide 22
Example: Find
L4
+ -
+
-

## Slide 23
+ -
+
-
L4
Solution:
Assign loop current
Assign resistor voltages
Express in terms of :
(E1)
Use KVL to make equation for the voltages:
(E2)
Plug (E1) into (E2) to obtain an equation for :
, by (E1)
To find apply KVL on right-side loop
The loop current is not asked.
But you still need to use it as a key variable and make an equation for it using KVL.
(E2)

## Slide 24
Practice 3: Find
R4
+ -
-+
+ -

## Slide 25
Practice 4: Find and
0.5v0
5A
3
R4

## Slide 26
Variation of the circuit:
0.5v0
5A
3
R4
0.5v0
5A
Add some resistors:
By the dependent current source,
(E2)
By KCL, (E1)
By Ohm’s Law:
(E3)
Plug (E2) and (E3) into (E1),
You have the same relationship among .
Thus the answers are not changed.
But the power supplied by the sources will be different.
For both circuits:

## Slide 27
Practice 5: Find and the power supplied by 6A source
2
6
4
2
0.5v0
6A
4
4
R4