## Slide 1
Test 1 Results:
54 students took the test
Average: 12.99 (64.95%)
6 students received 20 (100%)
12 students received > 18 (90%)
18 students received < 12 (60%)
Lowest scores: 0, 0, 0.2, 1, 2.5, 2.7, 3.7

## Slide 2
Chapter 3 Methods of Analysis: Nodal analysis and Mesh analysis
Basic concepts for nodal analysis:
Node voltage and ground
Definition: The ground for a circuit is defined as the point (or node), where the voltage = 0.
Symbols for the ground:
Node voltage at any other point is defined as the voltage drop from this point to the ground.
vg=0
va
With node voltage defined this way, the voltage drop between any two points is simply the difference of two node voltages.
vg=0
va
vb
By KVL, vab+vb-va=0
vab= va-vb
L8
Voltage at +
Voltage at -
Also called reference,
or, datum node

## Slide 3
vg= 0
vd
vc
vb
va
Along right loop:
All items cancelled. KVL automatically satisfied.
This is due to the assignment of node voltage and
that the voltage between any two points is the difference of two node voltages.
KVL automatically satisfied:
L8

## Slide 4
Pick node voltages as key variables.
Express everything else in terms of node voltages,
such as branch voltage, currents.
Then apply KCL at the nodes to form equations for node voltages.
A typical node:
KCL at center node:
R2
R1
vb
va
vc
+ vac -
+ vcb -
Main Idea of nodal analysis:
Express resistor currents in terms of node voltages
An equation for node voltages
L8

## Slide 5
One key step in nodal analysis:
Express the current through a resistor in terms of node voltages.
R
vb
va
Assign vR so that passive sign convention is satisfied. Then
Observation:
The current enters at va and exits at vb.
In the future, vR will not be assigned.
L8
General rule:

## Slide 6
Example: A circuit with only current sources. We need to find the current through each resistor.
R1
R3
R2
I2
I1
L8
For nodal analysis: No matter what is asked, you must
1) Assign node voltages,
2) Make equations for node voltages
3) Solve the equations
4) Then find what is asked

## Slide 7
Solution: Additional variables need to be assigned.
R1
R3
R2
I1
v1
v2
only three nodes.
How many nodes?
Step 1: pick the ground.
Assign node voltages, v1, v2.
Step 3: Apply KCL at each node
At
(1)
At
Express the currents in terms of node voltages:
Step 2: Assign resistor current
with reference direction,
Plug (*) into (1), (2), respectively,
L8
Recall:

## Slide 8
The reference direction of currents can be arbitrarily assigned.
Then the signs of and are reversed:
R1
R3
R2
v1
v2
When apply KCL at each node, the sign for also reversed
At v1:  (1)
At v2:  (2)
Plug (*) into (1), (2), respectively,
we obtain the same equations
Reversing the direction does not change the equations for node voltages.
Let us reverse and
L8

## Slide 9
Step 1: pick the ground. Assign node voltages for the remaining n nodes: v1, v2, …, vn
Step 2: Assign resistor currents with reference direction, i1,i2,…, Express them in terms of node voltages.
Step 3: Apply KCL at each of the node to obtain n equations for all branch currents. Then plug in the expressions from step 2, to obtain n equations for the n node voltages.
Step 4: clean up the equations, solve for the voltages v1, v2, …, vn and compute whatever is asked. Since all variables can be expressed in terms of these node voltages.
Summary of steps in nodal analysis.
Suppose that the circuit has n+1 nodes and has only current sources.
For circuit with only current sources, every branch current is either given, or, can be expressed in terms of node voltages.
L8

## Slide 10
Example: Find using nodal analysis
6Ω
5A
10A
v1
v2
2Ω
4Ω
The ground and node voltages already assigned.
Express resistor currents:
Apply KCL at the nodes:
At :
At :
(1)
(2)
Plug (*) into (1), (2)
(1a)
(2a)
L8
;
;
(*)

## Slide 11
8Ω
3A
v1
v2
i1
ix
i3
Example: A circuit with dependent current source. Form 3 equations for v1, v2, v3.
2Ω
4Ω
4Ω
i2
v3
2ix
has been assigned. Assign other resistor currents,
Express all resistor currents:
KCL at
KCL at
KCL at
Plug in current expression:
(1)
(2)
(3)
L8

## Slide 12
R8
4Ω
6A
4Ω
8Ω
3A
Practice problem 1:
Find by using nodal analysis method

## Slide 13
R8
3Ω
4A
i1
2Ω
1Ω
5A
3i1
Practice problem 2:
Find by using nodal analysis method.
How many node voltages?

## Slide 14
R8
2Ω
20A
i1
2Ω
4Ω
10A
Practice problem 3: Form 3 equations for
5A
1Ω
4Ω

## Slide 15
L9
Nodal analysis
Basic concepts: node voltage and ground
  Voltage between any two points is the difference of two node voltages
va
vb
v = va - vb;
va: voltage at +
vb: voltage at -
Basic step: Express resistor current in terms of node voltages:
vb
R
va
i
Basic idea: use KCL to form equations for node voltages

## Slide 16
L9
What if we have a voltage source?
+ -
5V
is
va
vb
A: is can not be expressed in terms of only va and vb
is
va-vb
5
0
is can be anything.
Q: How to express is in terms of va and vb ?

## Slide 17
L9
§ 3.3 Nodal Analysis with voltage sources
Case 1: The voltage source is connected to the ground
Three non-reference nodes: v1, v2, v3
At v2, i1-i2-i3= 0
At v3, i3+i4= -2
2A
10V
+
-
6
4
2
4
v1
v2
v3
i1
i4
i3
i2
is
At v1, is-i1-i4= 0
But is can’t be expressed in terms of v1
Get stuck here
v1=?
Do we really need a third KCL equation at v1?
How many unknown node voltages?
So we only have two unknowns, v2 and v3
(1) and (2) are sufficient to solve for v2 and v3

## Slide 18
L9
Case 2: One voltage source is not connected to the ground -- A floating voltage source
5V
10V
+
-
4
6
8
2
v1
v2
v3
i1
i4
i2
is
+ -
i3
Now we know v1=10V
Only two equations are needed for v2 and v3
KCL at v2: i1- i2 - is= 0 (1)
KCL at v3: i4- i3+ is= 0 (2)
Same trouble with is,
can’t be expressed in terms of v2, v3
Approach:
Neither (1) nor (2) would yield an equation for v2, v3
Add up (1) and (2): i1-i2+i4-i3= 0 (3)
What is this equation (3)?
(3) is obtained by applying KCL
at the closed boundary
5V
10V
+
-
4
6
8
2
v1
v2
v3
i1
i4
i2
is
+ -
i3
It includes both nodes v2 and v3
A supernode

## Slide 19
L9
In the future, we don’t apply KCL at each node connected to a voltage source (such as (1), (2)), then add them up.
We directly make a supernode and apply KCL at the supernode
5V
10V
+
-
4
6
8
2
v1
v2
v3
i1
i4
i2
is
+ -
i3
The currents:
Plug in current expressions
Need a second equation for v2 and v3
It comes from the 5V voltage source:
v2-v3=5 (Eq2)
Combining (Eq1) and (Eq2), v2 and v3 can be solved.
KCL at the super node: i1-i2+i4-i3= 0 (3)
v2 = 9.2V; v3=4.2V

## Slide 20
L9
General steps for nodal analysis with floating voltage sources:
Step 1: Choose ground and assign node voltages
Step 2: Assign resistor currents with reference direction, express them in terms of node voltages
Step 3: Form super node to combine two or more nodes. The purpose is to avoid the current of a voltage source in a KCL equation. The super node is made such that the closed boundary does not intersect a voltage source.
+ -
i1
i3
i4
i2
10V
v1
v2
KCL at super node:
i1- i2 - i3+i4= 0
Additional equation:
v1-v2=10
KCL at super node:
i1- i2 - i3= 0
Additional equation:
v1-v2=3ix
+ -
i1
i3
i2
3ix
v1
v2
is
Be careful: is≠ 3ix
Never make equation like: i1-3ix-i3= 0
3ix is a voltage,
not current
Step 4: clean up and solve equations

## Slide 21
L9
Example: Find i0 using nodal analysis. What is the power supplied by the 10V voltage source?
6S
10V
2A
4A
5S
3S
v1
v2
v3
i0
i1
i2
+ -
Solution:
Express resistor currents:
Note that the conductance is given, not resistance
Need to combine nodes at to form a super node
KCL at super node
At
(1)
(2)
The 3rd equation comes from the 10V voltage source:
(3)

## Slide 22
L9
How to find the power supplied by the 10V voltage source?
6S
10V
2A
4A
5S
3S
v1
v2
v3
i0
i1
i2
+ -
We have obtained
With these node voltage, everything can be solved
To find the power by the voltage source,
We need the current coming out of the positive terminal
How to find
By KCL at
Power supplied by 10V = 10

## Slide 23
L9
Example: Form 3 equations for the 3 node voltages
4V
4A
- +
+
-
Assign resistor currents:
KCL at supernode
KCL at
By
+ -
0
(equ3)
(equ1)
(equ2)

## Slide 24
R9
Practice 4: Form 3 equations for the three node voltages
4Ω
10V
5A
i4
i1
+ -
2Ω
2Ω
8Ω
i2
i3
v1
v2
v3

## Slide 25
R9
Practice 5: Form 4 equations for the four node voltages
2Ω
20V
10A
ix
i5
i2
+ -
+ -
9ix
6Ω
3Ω
4Ω
1Ω
i4
i3
v1
v2
v3
v4

## Slide 26
R9
Practice 6: Find
2Ω
19V
ix
i3
i2
+ -
3ix
4Ω
3Ω
3Ω
i1
v1
v2
v3
+
-