## Slide 1
L12
Chapter 4 Circuit Theorems
From Chapter 2: Basic laws -- Foundations.
From Chapter 3: Mesh analysis, Nodal analysis.
Systematic tools, can be used for complex circuits.
More useful tools to be learned in Chapter 4:
Linearity
Superposition
Source transformation
Thevenin’s Theorem
Norton’s Theorem
Maximum power transfer
Could be more tricky than Chapters 2,3.
There may exist several solutions to one problem
Need to develop insight to plan solutions ahead and identify the simplest solution

## Slide 2
L12
§4.2 Linearity
Basic concepts:
Input, output
Input: the cause, or excitation,
+ -
vs
Is
Output: voltage or current of any element
i
Is
Vs
+
-
6
4
2
4
5
7
12
i0
Example:
Two inputs
Vs, Is
Two outputs:
i0, v0
You can imagine pulling out the inputs, outputs and put the rest inside a box

## Slide 3
L12
Pull out the inputs, outputs and put the rest inside a box
Resistive circuit
6
i0
+
-
Vs
Is
Circuit System
Vs
Is
i0
v0
More abstract form
Input
output
First consider a circuit with one input, one output:
Circuit System
Input
output
Input output relationship can be described by a function

## Slide 4
L12
Input output relationship:
Circuit System
Input
output
Input : can be ,
Output : can be of any element
Linearity:
Two implications:
Linearity = homogeneity + additivity
Homogeneity:
If x1  y1,
then ax1  a y1
Additivity:
If x1  y1,
x2  y2,
then x1+ x2  y1+ y2
The input output relationship is said to be linear if for a certain constant .

## Slide 5
L12
Linear circuit:
the input-output relationship of a resistive circuit is linear.
Resistive circuit
i0
+
-
Vs
+ -
Resistive circuit
i0
Is
+ -
vo=k1Vs
i0=k2Vs
vo=k3Is
i0=k4Is
We first use one example to demonstrate linearity
Later on, we use this linear property to analyze circuits
Linearity is the simplest relationship between input and output
It is predictable: double efforts  double results
If
Then

## Slide 6
L12
Example:
Vs
+
-
8
6
2
4
I0
+
-
4
i1
i2
Input: Vs
Output: I0
A resistive circuit.
There exists a such that
I0=Vs
What is ?
Use mesh analysis to find .
Assign mesh currents i1, i2.
vx=2i1
 3vx= 6i1
KVL along mesh 1:
2i1+4(i1-i2)+Vs+6i1=0
 12i1-4i2= -Vs (1)
KVL along mesh 2:
8i2- 3vx+4i2-Vs+4(i2-i1) = 0
 -10i1+16i2 = Vs (2)
8i2- 6i1 +4i2-Vs+4(i2-i1) = 0
I0 = i2= Vs
I0= i2
)
Compare with
I0=Vs
(1)*5+(2)*6 

## Slide 7
L12
For this circuit, the input output relationship is derived by solving the output from the input
Given input  find output,
The direct approach
For some circuit, it is more convenient to find the input from the output.
Given output  find input,
The backward approach
Linear Circuit
Input
output
for a certain
How to find ?
If you know any pair of input and output,
Then
In general,
Just need one pair
to determine
Direct approach:
Assume , find
Backward approach:
Assume , find

## Slide 8
6
+
-
4
Practice 20: Find Vs for the circuit
10
9
I1=2A
R7
A practice problem from Chapter 2:
is the input, the cause
is the output, the result
Assume
6
+
-
4
10
9
I1=2A

## Slide 9
L12
Example:
Input:
Output:
Find such that
Use backward method
Assume ,
You may assume to be any number.
6
7
2
4
3
5
With solved, you have

## Slide 10
L12
Solution: Assign additional variables as in the following circuit:
Starting with I0=1A
By Ohm’s law: v0=5I0=5V; v1=3I0=3V
By KVL: v2=v0+v1=5+3=8V
By Ohms Law: I1=v2/4=2A
By KCL at v2: I2=I0+I1=1+2=3A
By (*): v3=v2+2I2=8+2*3=14V
By Ohms Law: I3=v3/7=14/7=2A
By KCL at v3: Is=I2+I3=3+2=5A
6
7
2
4
3
5
I0
Is
I1
Is
I3
I2
v2, v3 are node voltages
I0=1A
Is=5A
Conclusion:
The input-output relationship is
I0=Is= 0.2Is
If Is=15A, then
I0=0.2*15=3A
If Is=10A, then
I0=0.2*10=2A
With I0=0.2Is, you can find output Io for any input Is
You can also find the input for any output

## Slide 11
L12
A simple demonstration:
6
7
2
4
3
5
Is
Suppose
For
What if is replaced by
6
7
2
4
3
5
Vs
For

## Slide 12
L12
§4.3 Superposition
-- About the relationship between one output and several inputs
Superposition principle:
the voltage across (or current through) an element in a
linear circuit, is the sum of voltage/current due to each independent source alone.
i0
Is
+ -
+ -
Vs
i1
Is
+ -
Due to Is alone: turn off
Set Vs= 0  replace voltage source with short circuit
i2
+ -
+ -
Vs
v0= v1+v2
i0= i1+ i2
Due to Vs alone: turn off
Set Is= 0  replace current source with open circuit

## Slide 13
L12
Key points: when you examine the effect due to one source,
turn off the other sources
Turn off voltage source with short circuit
Turn of current source with open circuit

## Slide 14
L12
Example : Find the output v.
+
-
6V
3A
4Ω
8Ω
Step 1: Due to 6V alone
– turn off 3A with open circuit
Step 2: Due to 3A – turn off 6V with short circuit
By voltage division:
v = v1+v2 = 2+8=10V
+
-
6V
4Ω
8Ω
3A
4Ω
8Ω
By equivalent resistance and ohm’s law
Superposition breaks down a circuit into several circuits with only one independent
source – typically can be solved with simple methods in Chapter 2.

## Slide 15
R12
Practice 1: Find v0 for Vs=27V by linearity
2
3
4
3
4
2
Vs
+
-
Step 1: Find k such that v0=kVs by assuming v0= some value
Step 2: For Vs=27V, v0= k Vs

## Slide 16
R12
3A
4Ω
4Ω
Practice 2: Find i using linearity
8Ω
3Ω
i

## Slide 17
R12
+
-
12V
3A
4Ω
4Ω
Practice 3: Find i using superposition.
+ -
24V
8Ω
3Ω
i

## Slide 18
R12
+
-
6A
4Ω
4Ω
Practice 4: Find i using superposition.
24V
3Ω
i
1Ω

## Slide 19
L13
+
-
7V
7A
4Ω
8Ω
Example: Find I0 using superposition.
6Ω
3Ω
I0
Due to 7V:
Due to 7V: replace 7A with open circuit
Due to 7A: replace 7V with short circuit
7A
4Ω
8Ω
3Ω
I2
Due to 7A:
6Ω
+
-
7V
4Ω
8Ω
3Ω
I1
6Ω

## Slide 20
L13
7A
4Ω
8Ω
3Ω
I2
Due to 7A:
6Ω
7A
4Ω
8Ω
3Ω
I2
6Ω
7A
4Ω
8Ω
3Ω
I2
6Ω
4Ω
6Ω
3Ω
8Ω
7A
I2
I2
4Ω
7A
10Ω

## Slide 21
L13
+
-
7V
4Ω
8Ω
3Ω
I1
Due to 7V:
6Ω
with respect to
/
By current division:
Going back to the original circuit:

## Slide 22
L13
Example: Find vab using superposition:
+
-
+ -
10Ω
2A
3vab
4V
+
-
+ -
10Ω
3v1
Due to 4V
4V
+ -
10Ω
2A
3v2
Due to 2A
For circuit with dependent sources, keep the dependent sources.
They cannot be turned off . They are not input
Superposition with dependent sources:
By KVL: ,

## Slide 23
L13
§ 4.4: Source transformation
A general situation:
you can separate a circuit as the connection of two parts.
Circuit A
Circuit C
i
For circuit A, you can obtain a function v = f (i)
If there is another circuit B, with the same vi relationship,
You can replace Circuit A with Circuit B without affecting Circuit C
Circuit B
Circuit C
i
All variables in Circuit C are unchanged,
But the variables in Circuit A may not exist in Circuit B.
Sometimes you need to replace a complex circuit with a simpler one; as with Thevenin’s equivalent
Sometimes with one which is more convenient for analysis as with source transformation
You may need to make change to one part,
But want to ensure this change does not affect the other part

## Slide 24
L13
Compare the two connections:
What is the vi relationship for each circuit?
How to express in terms of ?
+
-
is
vs
R1
R2
Circuit A:
Circuit B:
i
i
iR
By KVL,
v = vs-vR= vs-R1i
By KCL, iR= is-I
v = R2iR= R2is- R2i
v = vs-R1i
v = R2is- R2i
To have the same vi relationship:
R1=R2, Vs=R2is

## Slide 25
L13
Conclusion:
The following two connections are equivalent
If you replace one with another, the rest of the circuit will not be affected.
However, be careful:
The voltages across resistor R in the two circuits are different;
The currents through R in the two circuits also different.
+
-
vs
R
i
R
i
is
vs= Ris
iR

## Slide 26
L13
Extension to dependent sources:
The following two connections are equivalent
vs
R
i
R
i
is
vs= Ris
+
-
For example, if is= kvx, then vs=Ris=Rkvx
If vs= ki0, then is=ki0/R
The rule: if you put the two sources side by side, the arrow of the current source points
from – to + of the voltage source

## Slide 27
L13
+
-
vs
R
i
R
i
is
vs= Ris
vs
R
i
R
i
is
+ -
All equivalent

## Slide 28
L13
+
-
12V
3A
4Ω
2Ω
8Ω
3Ω
Example: Find the voltage v0
using source transformation
a
b
Caution:
Need to keep the two nodes “a” and “b” so that v0 is kept after every change
b
After these transformations,
4Ω and 2Ω can be combined,
3Ω and 8Ω can be combined.
Reducing the number of elements
4Ω
2Ω
8Ω
3Ω
a
6Ω
8Ω
3Ω
a
b
When everything in parallel, you can rearrange the elements without changing the voltage and branch current.
4A
2A

## Slide 29
L13
2A
4A
6Ω
8Ω
3Ω
a
b
When everything in parallel, you can rearrange the elements without changing the voltage and branch current.
2A
b
4A
6Ω
8Ω
3Ω
a
2A
1.6Ω
a
b
v0=3.2V

## Slide 30
L13
+
-
18V
6V
2Ω
2Ω
4Ω
+
-
0.25vx
18V
2Ω
2Ω
4Ω
+
-
vx
+ -
3A
Approach 1:
Convert to a circuit with one loop.
3V
18V
1Ω
4Ω
+
-
vx
+ -
+
-
Express
KVL around loop:
Plug in
Example: Find vx

## Slide 31
L13
+
-
18V
6V
2Ω
2Ω
4Ω
+
-
0.25vx
18V
2Ω
2Ω
4Ω
+
-
vx
+ -
3A
2Ω
2Ω
4Ω
3A
Combine parallel resistors
4Ω//2Ω//2Ω=0.8Ω
Combine parallel current sources
Approach 2: Convert to a circuit with two nodes.
0.8Ω
vx=7.5V

## Slide 33
R13
9V
6Ω
2Ω
5Ω
Practice 5: Find v0 using source transformation
+
-
9v0
+
-
3Ω

## Slide 34
R13
3A
2Ω
2Ω
10V
2Ω
+ -
4A
2A
3Ω
Practice 6: Find v0 using source transformation

## Slide 35
R13
8V
1Ω
4Ω
Practice 7: Find I0 using source transformation
+
-
v0/3
6Ω
I0