## Slide 1
L14
§ 4.5 Thevenin’s Theorem
A common situation: Most part of the circuit is fixed, only one element is variable, e.g., a load:
i0
+ -
+ -
The fixed part, a two terminal circuit,
can be very complex.
How the variable part affects vo, io, or the power?
By Thevenin’s theorem, the complex two terminal circuit can be replaced with a simple circuit. Making the analysis very easy
Thevenin’s theorem is the most important result in Circuit Theory.
It will be a main tool for Chapters 7, 8.

## Slide 2
L14
Thevenin’s theorem: Every linear two terminal circuit can be made equivalent to the series connection of a voltage source and a resistor.
Same vi relationship
i
+ -
+ -
i
+
-
Vth
Rth
Vth: Open circuit voltage across the
two terminals
i=0
+ -
+ -
Also called Voc
Rth: equivalent resistance with respect to the two terminals when all independent sources are turned off
Case 1: No dependent source. Rth=Req (as in Chapter 2)
Case 2: With dependent source. Need to supply an external independent source at the two terminal. Then Rth is the ratio between the voltage and current.

## Slide 3
L14
Example: What is the relationship
between RL and i?
+
-
32V
2A
4Ω
12Ω
1Ω
b
a
RL
i
Replacing the part to the left of “a”, “b” by Thevenin’s equivalent
+
-
Vth
Rth
b
a
RL
i
Clear relationship:
Key point: Vth=?, Rth=?
Solution:
Vth is the open circuit voltage.
+
-
32V
2A
4Ω
12Ω
1Ω
a
i1
Assign mesh current i1
KVL along the mesh: 4i1+12(i1+2)=32
i1=0.5A
Vth=12(i1+2)=30V
For Rth, turn off all independent sources:
4Ω
12Ω
1Ω
Rth=1+4//12
=4
i=0
+ 0V -

## Slide 4
L14
Approach 2: Find by source transformation
+
-
32V
2A
4Ω
12Ω
1Ω
b
a
10A
3Ω
1Ω
a
b
8A
2A
4Ω
12Ω
1Ω
a
b
30V
3Ω
1Ω
a
b
+
-
+
-
b
a

## Slide 5
L14
Case 2: There are dependent sources
Vth: The same as case 1, the open circuit voltage
For Rth:
Turn off all independent sources.
+ -
i0
+ -
+ -
+
-
i0
v0
or,
Give any number for i0, e.g., 1A, 2A, 10A,
Solve for v0
Give any number for v0, e.g., 1V, 2V, 20V,
Solve for i0
2. Connect the two terminals to a current/voltage source
3. Solve for the voltage/current of the source
Note: assigned by active sign convention.

## Slide 6
L14
Be careful, v0 and i0 are assigned according to active sign convention with respect to the source (passive sign convention for ).
Explanation: as the independent sources are turned off, the two terminal circuit behaves like a single resistor.
i0
i0
+
-
Rth
Rth

## Slide 7
L14
Example:
Find Rth, Vth for the two terminal circuit
+
-
30V
6Ω
3Ω
a
2vx
b
For Vth:
a
Vth= vx
+
-
30V
6Ω
3Ω
2vx
Use nodal analysis
Pick ground. vx is the node voltage
vx
b
KCL at node vx:
vx= 2V
Vth=2V
For Rth: turn off 30V with short circuit.
Approach 1: connect to voltage source v0=1V,
6Ω
3Ω
a
2vx
vx
+
-
v0=1V
i2
i0
i1
KCL at node vx:
i0= i1+i2+2vx
Given vx=1V
Need to find

## Slide 8
L14
Approach 2: connect to current source i0=1A,
KCL at node v0:
i1+i2+2vx=1
6Ω
3Ω
a
2vx
v0
i0=1A
i2
i1
v0= vx
v0=0.4
Two approaches yield the same Rth.

## Slide 9
24V
4
4
12
4
- +
+ vx -
0.5vx
Example: Find for the two terminal circuit
24V
4
4
12
4
- +
+ vx -
0.5vx
For
0A
By KVL,
0A
0A
By voltage div

## Slide 10
24V
4
4
12
4
- +
+ vx -
0.5vx
For turn off 24V, Supply a 1A current source.
Find the voltage across the current source
1A
By KVL,
1A
2A
//12)
4
4
12
4
+ vx -
0.5vx
1A
-1A
Then

## Slide 11
Example: Find Thevenin’s equivalent with respect to terminals “a” and “b”.
14V
8
4
2.5A
6
4
a
b
- +
8
8
16
open circuit voltage
14V
8
4
2.5A
6
4
a
b
- +
8
8
16
By current division
//(8+8+6+8)=16
8
4
6
4
a
b
8
16
8

## Slide 12
Example: Find Thevenin’s equivalent circuit with respect to terminals “a” and “b”
3
- +
6
2
12
3
a
b
For , the open circuit voltage,
since there is no independent source ,
all voltages and currents are 0,
For , need to supply the two terminal with independent current or voltage source.
3
- +
6
2
12
3
a
b
Set , need to find . Then
Use source transformation

## Slide 13
R14
Practice 1: Find Rth, Vth for the two terminal circuit
+
-
5V
5A
3Ω
4Ω
2Ω
4Ω
a
b

## Slide 14
R14
Practice 2: Find Rth, Vth for the two terminal circuit
4Ω
2Ω
a
2ix
b
ix

## Slide 15
R14
5Ω
2Ω
a
2vx
Practice 3: Find Rth, Vth for the two terminal circuit
10V
3Ω
2Ω
b
+
-

## Slide 16
L15
§4.6 Norton’s Theorem
Norton’s theorem: Every linear two terminal circuit can be made equivalent to the parallel connection of a current source and a resistor.
IN: Short circuit current from “a” to “b”, RN: same as Rth
i
+ -
+ -
i
IN
RN
a
b
b
a
i
+
-
Vth
Rth
Since the same circuit is also equivalent to Thevenin’s
By source transformation,
RN=Rth, Vth=RthIN,
IN=Vth/Rth
You can get Thevenin’s equivalent first, then use source transformation to get Norton’s equivalent, or vice vesa

## Slide 17
L15
Example:
Find the Norton’s equivalent
+
-
12V
2A
4Ω
8Ω
5Ω
b
8Ω
a
For IN, short circuit “a”, “b”
Be careful: a resistor in parallel with short circuit does not take any current.
It can be discarded.
+
-
12V
2A
4Ω
8Ω
5Ω
b
IN
8Ω
a
voltage across is 0.
KVL along center mesh:
8IN+8IN-12+4(IN-2)=0
IN=1A
For RN, turn off 2A and 12V sources:
4Ω
8Ω
5Ω
b
8Ω
a
RN=5//(8+8+4)=4
I1
IN
2A
What is the relationship between

## Slide 18
L15
Approach 2:
use source transformation
+
-
12V
2A
4Ω
8Ω
5Ω
b
8Ω
a
20V
4Ω
8Ω
5Ω
b
8Ω
a
+
-
1A
20Ω
5Ω
b
a
3A
2A
4Ω
8Ω
5Ω
b
8Ω
a
1A
4Ω
b
a

## Slide 19
L15
§4.8 Maximum power transfer
i
+ -
+ -
a
b
RL
Linear circuit connected to a variable load RL
Power consumed by load:
Question: for what value of is maximized?
Note that the current also depends on .
Key point: find the exact relationship between and RL.
Main tool:
Thevenin’s and Norton’s theorem
Applications examples:
Radio transmitter - maximize power delivered to the antenna or transmission line
Grid tied inverter - maximize power delivered to the grid
Electric vehicle - maximize power delivered to drive motor

## Slide 20
L15
By Thevenin’s theorem, the two terminal circuit can be replaced with a voltage source in series with a resistor:
i
+
-
Vth
Rth
RL
Clear relationship:
As

## Slide 21
L15
A pure math problem: find RL so that p is maximized.
p
RL
pmax
R0
At the maximal point,
For dp/dRL= 0, we must have RL=Rth
At RL=Rth,

## Slide 22
L15
Conclusion:
Maximal power is transferred to the load when RL=Rth, and the maximal power is
When the Norton’s equivalent is used, similar result:
Conclusion:
Maximal power is transferred to the load when RL=RN, and the maximal power is

## Slide 23
L15
Example:
Determine R so that maximal power is delivered.
Also find the maximal power.
+
-
R
20V
4Ω
0.5vx
15Ω
6Ω
10Ω
Solution: Need to find Vth and Rth with respect two the two terminals of R.
For Vth, disconnect R
Since i=0, vx= 0. 10 and 15 in series
By voltage division
+
-
20V
4Ω
0.5vx
15Ω
6Ω
10Ω
i=0
i=0
Also since i=0, 0.5vx=0 flows through 4Ω.
Thus
v2= 0V
By KVL,
Vth=vx+v1-v2=0+12+0=12V

## Slide 24
L15
For Rth, turn off 20V, but keep 0.5vx dependent source.
Because of the dependent source, supply an external current source i0= 1A. (you may also try a voltage source and compare)
Need to find v0 across the 1A current source
(Active sign convention)
Assign current i2 for 4Ω
By KCL, i2=0.5vx-1. Thus
v2= 4(0.5vx-1)
= 4(3-1)=8V
vx=6i0=6V
4Ω
0.5vx
15Ω
6Ω
10Ω
i0=1A
1A
i2
Finally, The maximal power is delivered when R=Rth=4Ω.
The maximal power is

## Slide 25
Example: Find Thevenin’s equivalent with respect to terminals “a” and “b”.
15V
+
-
3
3
1.5A
6
4
a
b
15V
+
-
3
3
1.5A
6
4
a
b
//
3
3
6
4
a
b
KVL along mesh 1:

## Slide 26
L15
Question: Any relationship between the following circuits?
i
R
+
-
Vs
Is
i
R
Norton’s equivalent:
Thevenin’s equivalent:
Is
i
i
+
-
Vs
0
Any resistor in series with current source can be discarded
Any resistor in parallel with voltage source can be discarded
Illegal to open circuit
Illegal to short circuit

## Slide 27
R15
Practice 4: Find the Norton’s equivalent
+
-
40V
3A
20Ω
40Ω
10Ω
a
b

## Slide 28
R15
RL
ix
Practice 5: Find the value of RL so that maximum power is delivered. Also find the maximum power.
+
-
4V
2Ω
3ix
2Ω
1Ω
+
-

## Slide 29
R15
60Ω
Practice 6: Find the unknown RL so that maximum power is delivered. Also find the maximum power.
40V
80Ω
RL
20Ω
40Ω
+ -

## Slide 30
Chapter 4 Review
  Linearity
  Source transformation
  Superposition
  Thevenin’s Theorem
  Norton’s Theorem
  Maximum power Transfer

## Slide 31
Linearity:
the input-output relationship of a resistive circuit is linear.
Resistive circuit
i0
+
-
Vs
+ -
Resistive circuit
i0
Is
+ -
vo=k1Vs
i0=k2Vs
vo=k3Is
i0=k4Is
Linear Circuit
Input
output
for a certain
How to find ?
If you know any pair of input and output,
Then
In general,
Backward approach:
Assume , find

## Slide 32
Example 1: Find for . Compute for .
12
10
7
4
16
2
4
4
4
5

## Slide 33
Solution: Find for . Set the bottom node as ground
12
10
7
4
16
2
4
4
5
4
For
,
If ,
If ,

## Slide 34
Superposition
Superposition principle:
the voltage across (or current through) an element in a
linear circuit, is the sum of voltage/current due to each independent source alone.
i0
Is
+ -
+ -
Vs
i1
Is
+ -
Due to Is alone: turn off
Set Vs= 0  replace voltage source with short circuit
i2
+ -
+ -
Vs
v0= v1+v2
i0= i1+ i2
Due to Vs alone: turn off
Set Is= 0  replace current source with open circuit
Key points:
Turn off voltage source with short circuit
Turn of current source with open circuit

## Slide 35
Example 3: Use superposition to compute v0
9W
30W
4W
30V
3A
- +
18W
9W
30W
4W
3A
18W
Due to 3A
9W
30W
4W
3A
18W
30W
4W
3A
6W

## Slide 36
Due to 30V:
9W
30W
4W
30V
- +
18W
9W
30W
4W
30V
- +
18W
6W
34W
30V
- +
By voltage division:

## Slide 37
Source Transformation:
The following two connections are equivalent
+
-
vs
R
i
R
i
is
vs= Ris
iR
The following two connections are equivalent
vs
R
i
R
i
is
vs= Ris
+
-
The rule: if you put the two sources side by side,
the arrow of the current source points from – to + of the voltage source

## Slide 38
L13
+
-
12V
6Ω
3Ω
4Ω
1.5
8
6Ω
3Ω
4Ω
+ -
2A
6Ω
3Ω
12Ω
2A
Example : Compute : Use source Transformation to convert the circuit to one with only two nodes.
8
Use Nodal analysis method:
KCL at :

## Slide 39
Thevenin’s theorem: Every linear two terminal circuit can be made equivalent to the series connection of a voltage source and a resistor.
i
+ -
+ -
i
+
-
Vth
Rth
Vth: Open circuit voltage across the
two terminals
i=0
+ -
+ -
Also called Voc
Rth: equivalent resistance with respect to the two terminals when all independent sources are turned off
Case 1: No dependent source. Rth=Req (as in Chapter 2)
Case 2: With dependent source. Need to supply an external independent source at the two terminal. Then Rth is the ratio between the voltage and current.

## Slide 40
Norton’s Theorem
Every linear two terminal circuit can be made equivalent to the parallel connection of a current source and a resistor.
IN: Short circuit current from “a” to “b”, RN: same as Rth
i
+ -
+ -
i
IN
RN
a
b
b
a
i
+
-
Vth
Rth
Since the same circuit is also equivalent to Thevenin’s
By source transformation,
RN=Rth, Vth=RthIN,
IN=Vth/Rth
You can get Thevenin’s equivalent first, then use source transformation to get Norton’s equivalent, or vice vesa

## Slide 41
Maximum power transfer
i
+ -
+ -
a
b
RL
Linear circuit connected to a variable load RL
Power consumed by load:
Conclusion:
Maximal power is transferred to the load when RL=Rth, and the maximal power is
When the Norton’s equivalent is used, similar result:
Conclusion:
Maximal power is transferred to the load when RL=RN, and the maximal power is

## Slide 42
Example 4: Find the unknown resistance RL so that maximum power is delivered to it. Also find the maximum power.
18V
3
2
4
+
-
-
+
2
For , disconnect
18V
3
2
4
+
-
-
+
2
For , turn off 18V, supply current source
3
2
4
-
+
2
KVL along outer loop:
0.8,
,
When =2.025W