- (15 points) Determine the line integral of  from P1(-1,3,-2) to P2(2,4,1), where points are specified in rectangular coordinate system.

2.  (10 points) Find the Laplacian of the following scalar functions:

(a)

(b)

3. (25 points) Verify  Stokes’s theorem for the vector fieldout of the surface bounded by

4 (25 points) A parallel-plate capacitor has two dielectric filling regions between the plate, A1 = 1m^2, A2 = 4m^2, d = 2mm, V = 10Vignore Fringing field effect.

Determine:

- Electric field densities E1, E2 of the two regions.

The capacitance of the capacitor (hint: consider this as two parallel-plate capacitors in parallel)

- 5 (25 points) The x-y plane separates two magnetic media with magnetic permeability: , if we know

- if no surface current, determine:

if surface current  determine .

EE 16.360  Exam III

11/24/2003

Name:       _________________________

Signature: _________________________

# Text boxes

A2

A1

d

V

z

x, y plane