## Slide 1
1. Antireflection coating
n1
n2
n3
For the normal incidence from material with refractive index of n1, (1) show that to achieve antireflection from surface n2 and n3; (2) what is the thickness of the n2 layer?

## Slide 2
2. Incident angle for an optical fiber, numerical aperture (NA)
If the index of an optical fiber is n2 = 1.5 (glass) and n1 = 1.0 (air). Calculate the maximum allowed angle  for low loss transmission in an optical fiber. Sin() is called numerical aperture.
n2
n1
n1


90º-
Accepting cone

## Slide 3
3: effective refractive index
Waveguide thickness 5m, free-space wavelength 1.5m, using the normalized waveguide equation, calculate the effective refractive indices of each mode supported by the waveguide. You need to use your computer to calculate the values.
5 m
n2 = 1.6
n1 = 1.5
n1 = 1.5
 = 1.5 m

## Slide 4
5 um
n2 = 1.6
n1 = 1.5
n1 = 1.5
How many TE modes?
Calculate the effective index for each mode using the transmission matrix method. Please use your own codes.
Plot the mode profile for each mode
4. One slab wavguide
 = 1.5 um